## Slide 1: A preliminary study on empirical analysis of conducted EMI from electrical appliances
Ver1.2
23-03-2014
Planned Deadline for Poster: 26-03-2014

## Slide 2: Short forms and considerations
BGN: Background noise
PLL: Power load line meant for 15Amp loads
By default the frequency range is from 10Khz-1Mhz unless defined explicitly.

## Slide 3: Hardware Setup for < 5Amp loads

## Slide 4: Noise from CFL and BGN

## Slide 5: Observations
EMI noise is quite significant from 60Khz and stays for long.
Amplitude goes down from -90dBm to -100dBm with higher frequencies.
Even amplitude of harmonics is significant enough -100dBm.
In freq. range 600Khz - 1Mhz Vmin of noise amplitude is roughly 10dB higher then baseline noise.
Not very much sure but a slightly low cut-off HPF may give some more information in LF range.

## Slide 6: Noise from LEDTV and BGN

## Slide 7: Observations
EMI noise is completely suppressed by inbuilt EMI filter in current freq. range from 10hz to 1Mhz.
Hardly any change is noticed in visible spectrum.

## Slide 8: Noise from CFL and BGN

## Slide 9: Noise from LEDTV+CFL and BGN

## Slide 10: Observations
Current combination of LEDTV and CFL gave some nice results.
For ease of comparison same trace of CFL is copied above.
EMI noise is completely suppressed from 200Khz to 550Khz.
Amplitude of EMI noise(CFL) from 550KHz to 1Mhz is reduced by 10dB.
Similar was case for EMI from 10Hz to 200Khz range amplitude reduced by 10dB.

## Slide 11: Noise from Phonecharger and BGN

## Slide 12: Observations
EMI noise is completely suppressed by inbuilt EMI filter in current freq. range from 10hz to 1Mhz.
Hardly any change is noticed in visible spectrum.

## Slide 13: Noise from USRP and BGN

## Slide 14: Observations
EMI noise is completely suppressed by inbuilt EMI filter in current freq. range from 10hz to 1Mhz.
Hardly any change is noticed in visible spectrum.

## Slide 15: Noise from CFL and BGN

## Slide 16: Noise from USRP+CFL1 and BGN

## Slide 17: Observations
Current combination of USRP and CFL gave some nice results.
For ease of comparison same trace of CFL is copied above.
Amplitude of EMI noise(CFL) from 100KHz to 1Mhz is reduced by 15dB and at some points by 10dB.
In higher frequency range from 650Khz to 1Mhz hardly anything is visible almost whole noise spectrum is suppressed.

## Slide 18: Noise from USRP+CFL2 and BGN

## Slide 19: Observations
Same as previous one took another trace after some time to validate results.

## Slide 20: Noise from USRP+Phonecharger and BGN

## Slide 21: Observations
EMI noise is completely suppressed by inbuilt EMI filter in current freq. range from 10hz to 1Mhz.
Hardly any change is noticed in visible spectrum.

## Slide 22: Noise from CFL and BGN

## Slide 23: Noise from USRP+Phonecharger+CFL and BGN

## Slide 24: Observations
Current combination of USRP and CFL gave some nice results.
For ease of comparison same trace of CFL is copied above.
Amplitude of EMI noise(CFL) from 100KHz to 1Mhz is reduced by 8dB and at some points by 10dB.
In higher frequency range above 700Khz hardly anything is visible almost whole noise spectrum is suppressed.
One interesting change was in freq. range less than 100Khz EMI noise from CFL was increased by 5dB.

## Slide 25: BGN taken at two different time intervals

## Slide 26: Observations
Two traces of Background noise were taken to check consistency of noise as we are comparing noise with BGN in all plots.
Above results show that both the traces fairly overlap eachother and BGN is consistent with time.

## Slide 27: Noise from ATX power supply and BGN

## Slide 28: Observations
EMI noise is completely suppressed by inbuilt EMI filter in current freq. range from 10hz to 1Mhz.
Only some noise spikes have shown increase in amplitude in the visible spectrum.

## Slide 29: Noise from ATX power supply and BGN from 10Khz-3Mhz

## Slide 30: Observations
EMI noise is showed up when observation range was modified to 10hz to 3Mhz earlier upper limit was 1Mhz.
Some noise spikes have shown increase in amplitude from 600Khz to 1.75Mhz.
A nice change is visible in freq. range from 1.75Mhz to 2.75Mhz with a amplitude of roughly 3-4dB.

## Slide 31: Noise from Microwave(Turned on) and BGN

## Slide 32: Observations
EMI noise is completely suppressed by inbuilt EMI filter in current freq. range from 10hz to 1Mhz.
Hardly any change is noticed in visible spectrum.

## Slide 33: Noise from Microwave(1min mode) and BGN

## Slide 34: Noise from Microwave(10min mode) and BGN

## Slide 35: Noise from Microwave(4min mode) and BGN

## Slide 36: Observations
EMI noise taken from 3 operational modes of Microwave has shown a small but noticeable change in freq. range 400Khz to 1Mhz roughly 2-3dB.

## Slide 37: Noise from Microwave(Turned on) and BGN from 10Khz-3Mhz

## Slide 38: Observations
EMI noise shows a small change from 2.25Mhz to 2.75Mhz roughly around 2-3dB.
Earlier in while observing in 10Khz to 1Mhz range their was hardly any noticeable change.

## Slide 39: Noise from Microwave(Turned on) and BGN from 10Khz-3Mhz

## Slide 40: Noise from Microwave(1min mode) and BGN from 10Khz-3Mhz

## Slide 41: Noise from Microwave(10min mode) and BGN from 10Khz-3Mhz

## Slide 42: Observations
EMI noise taken from 2 operational modes of Microwave has shown a significant change in freq. range 1.8Mhz to 3Mhz compared to just turned on state of microwave.
Compared to both operational states even there is a small change in amplitude when operational in 10min mode then to 1 min mode in the same frequency spectrum.

## Slide 43: BGN taken at two different time intervals from 10Khz-3Mhz