## Slide 1: Sensing conducted EMI in power lines for appliance disaggregation
Highlights: Overview of NILM, Past work, Conducted EMI as a unique/deterministic aspect
Manoj gulati
Advisers: Dr. Amarjeet Singh and Dr. Shobha Sundar Ram

## Slide 2: Proposed work
To study unique and distinct features in conducted EMI generated by multiple electrical appliances.
Specific test cases:
Study impact of voltage fluctuations & building architecture on CE.
Study dissimilar features in CE during w/ and w/o load.
Study effect on CE of a single SMPS(EUT) for different loads.
Analyze features and unique aspects in CM CE and DM CE for different electrical loads.
Analyze response of EMI (constructive/destructive interference) w/o LISN.
Analyze low freq. disturbances due to different loads.
Try to differentiate among appliances with dual switching sections (i.e. PFC section and DC-DC convertor section).
*CE Conducted EMI *CM Common mode *DM Differential mode