## Slide 1: Sensing conducted EMI in power lines for appliance disaggregation
Highlights: Overview of NILM, Past work, Conducted EMI as a unique/deterministic aspect
Manoj gulati
Advisers: Dr. Amarjeet Singh and Dr. Shobha Sundar Ram

## Slide 2: Proposed work
To study unique and distinct features in conducted EMI generated by multiple electrical appliances.
Specific test cases:
Study impact of voltage fluctuations & building architecture on CE.
Study dissimilar features in CE during w/ and w/o load.
Study effect on CE of a single SMPS(EUT) for different loads.
Analyze features and unique aspects in CM CE and DM CE for different electrical loads.
Analyze response of EMI (constructive/destructive interference) w/o LISN.
Analyze low freq. disturbances due to different loads.
Try to differentiate among appliances with dual switching sections (i.e. PFC section and DC-DC convertor section).
*CE Conducted EMI *CM Common mode *DM Differential mode

## Slide 3: Experimental Setup-1
Mains
Power Supply
High Pass Filter (Fc = 50 KHz)
Flat Response 50KHz – 30Mhz
Attenuator
(To avoid risk to Signal Analyzer)
Signal Analyzer
Equipment under Test (Known type of SMPS)
Test Load (LCD/Laptop)
Line
Neutral
High Voltage
Components

## Slide 4: Experimental Setup-2
Mains
Power
Supply
High Pass Filter (Fc = 50 KHz)
Flat Response 50KHz – 30Mhz
Attenuator
(To avoid risk to Signal Analyzer)
Signal Analyzer
Equipment under Test (Known type of SMPS)
Test Load (LCD/Laptop)
Low Pass Filter (Fc = 60Hz)
To chop of HF disturbances
Line
Neutral
High Voltage
Components
High Voltage
Components

## Slide 5: Proposed Setup-1 (To study HF disturbances)
Mains
Power
Supply
High Pass Filter (Fc = 50 KHz)
Flat Response 50KHz – 30Mhz
Attenuator
Mains power supply provided to Building under test
Multiple combinations of SMPS and Non-SMPS loads
Low Pass Filter (Fc = 60Hz)
To chop of HF disturbances
High Speed ADC + MCU (Capable to push data to cloud)
Neutral
Line
High Voltage
Components
High Voltage
Components

## Slide 6: Proposed Setup-2 (To study LF disturbances)
Mains
Power
Supply
Low Pass Filter (Fc = 50 KHz)
Flat Response
0 Hz - 50KHz
Attenuator
Mains power supply provided to Building under test
Multiple combinations of SMPS and Non-SMPS loads
Low Pass Filter (Fc = 60Hz)
To chop of HF disturbances
High Speed ADC + MCU (Capable to push data to cloud)
Neutral
Line
High Voltage
Components
High Voltage
Components

## Slide 7: Power Supply Classification By SMPS Topologies
Topology | Applications | Power | Benefits | Negative aspects
Flyback | Cellphone chargers (<10W) Notebook adapters (<100W) CRT Power supplies (<150W) | <150W | Ease of implementation Well-Documented convertor. Operates on wide mains Large controller offer | High Peak currents Leakage inductance difficult to manage
Single switch forward | ATX power supplies (<250W) DC-DC convertors for telecom | <300W | Good cross regulation with coupled inductors. Good EMI signature. Low AC content, low conduction losses | Stress on power MOSFET. Difficult to operate on wide mains. Requires transformer reset. Duty cycle clamped to 50%
Two-Switch forward | ATX power supply (<500W) DC-DC convertor Telecom Servers(<500W) | 100-500W | Good cross regulation with coupled inductors. Good EMI signature. MOSFET stress clamped to Vin | Difficult to operate on wide mains. Requires transformer reset. Duty cycle clamped to 50% Requires high side drive.

## Slide 8
Topology | Applications | Power | Benefits | Negative aspects
Half-Bridge | ATX power supply (<500W) DC-DC convertor Telecom Servers(<500W) | 100-500W | Good cross regulation with coupled inductors. Good EMI signature. MOSFET stress clamped to Vin. Duty cycle <100% | Difficult to operate on wide mains. Requires high side drive. Cannot easily work with current mode.
Half-Bridge LLC | Medical power supplies LCD or plasma TV | <500W | Excellent EMI signature Can work in no load. Smooth waveforms, zero voltage switching (ZVS) possible. | High side drive Large RMS current Narrow mains operation. Dangerous short circuit.
Full bridge | Server and mainframe power supplies. High power DC-DC convertors for telecom. | >500W | Good cross regulation with coupled inductors. Resonant operation via phase shift. Good EMI signature. MOSFET stress clamped to Vin. Duty cycle <100% | Difficult to operate on wide mains. Requires two high side drive circuits. Four MOSFETs to drive.
Push-Pull | DC-DC convertors | <200W | MOSFETs control is ground referenced Duty cycle <100% | Voltage stress of 2Vin Center-tapped primary.
Source: Appendix1C(Pg-93) Switched Mode power supplies by Christophe P. Basso

## Slide 9: Current Status
Prepared PCB for HPF ver1.1 going to test it on 08-2-2014 with Low amplitude High freq. signals to observe freq. response on Signal analyzer.
Second test will be with 230VAC in controlled environment, initially with DSO then with Signal analyzer.
Preparing NILM survey to figure out what all approaches are currently being used to disaggregate appliance level information/ appliance states.
Improving upon appliance classification list to motivate my current research problem.

## Slide 10: Survey of NILM Papers (Not yet completed)
Will update by Sunday (9-2-2014)